## Slide 1: Couch Guardian
ThePerfect10

## Slide 2: Agenda
Team Introduction
Purpose, Motivation, Target Audience
System Implementation
Features
Non-Functional Requirements
Lessons Learned
Collaboration Tools
Product Demostration

## Slide 3: Team Introduction
Group Details
  Group 10 aka thePerfect10
  Couch Guardian smart device
  YouTube link: https://youtu.be/2tebSB6xQng
Team Members
  David Batson – Product Owner
  Tsz Shing Tsoi – Scrum Master
  Francis Iniobong John Ifon – Individual Contributor
  Alyssa Johnson – Individual Contributor

## Slide 4: Purpose, Motivation, & Target Audience
Purpose
Stop bad pet behavior
Motivation
Save pet owners money by preventing damage
Target Audience
Veteran and new pet owners
Pet owners with an interest in IoT
Log the bad behavior for rehabilitation measures
Notify the pet owner of the bad behavior happening

## Slide 5: System Architecture
Physical Components
IoT Integration
Software Structure

## Slide 6: Physical Components
Camera
Amplifier
LED
Speaker
Raspberry Pi

## Slide 7: IoT Integration
IBM Cloud Services
  IBM Cloudant (Apache CouchDB)
  IBM Watson IoT Platform
  Node-RED, including Node-RED Dashboard
Email Service
  Gmail

## Slide 8: IBM Cloudant (Apache CouchDB)
Views (MapReduce)
Search Indexes

## Slide 9: Node-RED
1. Monitor Signal from Watson IoT
2. Query IBM Cloudant Database
3. Process Data and Update Dashboard

## Slide 10: Node-RED Dashboard
https://cen5035group10.mybluemix.net/ui

## Slide 11: Software Structure
Written in Python using:
TensorFlow Lite -
  Object Detection model
    Ssd_mobilenet_v2_quantized_300x300_coco
  Detects: Dogs, Cats, Tables, Couches, Chairs
OpenCV -
  PiCamera and Image Processing
smtplib -
  Python library for email

## Slide 12: Device Features
Device placed in view of furniture to protect from pets
  More than 3 feet from item for full view
PiCamera is actively identifying objects in view
If a cat or dog is identified AND is overlaps with a couch, chair, or table:
  LED display on device notifies user that the device is active and working properly
  Sound plays from connected speaker
    Customized to pet type
  Email sends to user with a picture of the pet in action
  Log is sent to Watson IoT platform for Dashboard record
Dashboard illustrates progress in training pet to stay off of furniture

## Slide 13: Features for the Future
Automated activation of detection program on startup
LED notification of established internet connection
Web-site created to provide additional user features:
  Searchable photo and video storage
  User account to setup email
Faster FPS Object Detection
Better trained pet behavior model
Wireless Bluetooth speaker link
Novelty connection to a more active deterrent for pets
  Small flailing robot
  Roomba that will follow pet)

## Slide 14: Non-Functional Requirements
Usability
  Device is capable of monitoring a large room, unobtrusively, without risk to pet or human
Reliability
  Device identifies pets and furniture with 90% accuracy and issues sound and email notifications appropriately with little to no failure
Performance
  Device can identify several entities within a single frame and perform a response within 5 seconds of logged activation
Supportability
  Github repositories are maintained for multiple iterations of capability upgrades
Security
  Email and Watson Dashboard credentials are non public entities

## Slide 15: Lessons Learned
Remote collaboration has distinct challenges
  Knowledge gaps
  Scheduling concerns
Debugging with dependencies within modules and libraries
Developing new code and the organization needed

## Slide 16: Thank you